## Slide 1
Satellite-based monitoring of particulate matter pollution at very high resolution: the HOTBAR method Robin Wilson, Edward Milton & Joanna Nield
r.t.wilson@soton.ac.uk @sciremotesense

## Slide 2
Ground monitoring is not detailed enough

## Slide 3
“Health exposure needs tend to focus on spatial scales ranging from 1 to 100m ...neither surface monitoring or satellite measurements can deal with that spatial scale”
Hoff & Christopher (2009)

## Slide 4
“Health exposure needs tend to focus on spatial scales ranging from 1 to 100m ...neither surface monitoring or satellite measurements can deal with that spatial scale”
Hoff & Christopher (2009)
And… Martin (2008), Gupta et al. (2006), Loughner et al. (2007)…
We need high-res data!

## Slide 5: Radiative Transfer
Aerosols cause scattering
Path Radiance
Ground Radiance
Adjacent Radiance
But, we measure the sum!

## Slide 6: Radiative Transfer
Aerosols cause scattering
Path Radiance
Ground Radiance
Adjacent Radiance
But, we measure the sum!
How do we separate these?
Polarisation, Multi-temporal, Multi-angle…

## Slide 7: Haze Optimized Transform (HOT)
Blue
Red
Haze =
Aerosols
Zhang et al. (2002)
Distance ∝
Haze

## Slide 8
HOTBAR
Haze Optimised Transform based Aerosol Retrieval
Input: Landsat image
Estimate the Clear Line
Correct for land-cover effects
Link HOT values to AOT
Estimate PM2.5 concentrations
Output: PM2.5 image

## Slide 9: HOT to PM2.5
Start with a Landsat image
Estimate the Clear Line
Correct for land-cover effects
Link HOT values to AOT
Estimate PM2.5 concentrations
HOTBAR
Haze Optimised Transform based Aerosol Retrieval

## Slide 10: Estimating the Clear Line
The HOT set the Clear Line from a regression of a clear part of the image
BUT aerosols are everywhere!
We need Clear Pixels
  Created the LandsatAERONET dataset:
  Thousands of very accurately atmospherically-corrected pixels
  Range of land covers
  Easy to model any sort of atmospheric conditions

## Slide 12: Monte Carlo Regression
Clear Line depends on land cover
So, get land cover proportions (from a global land cover map like GlobCover)
Estimate Clear Line with a Monte Carlo Regression process

## Slide 13: Correcting for Land Cover effects

## Slide 14: Correcting for Land Cover effects
The HOT is not Land Cover invariant
We need to correct for this – how?
  Aerosols mix in the atmosphere
  → no sharp boundaries
  Land covers often have sharp boundaries
Look for sharp boundaries, correct the pixel values inside these ‘objects’
→ Object-based Image Analysis

## Slide 15
Original
Corrected
TODO: Update these images!

## Slide 16: Link HOT to Aerosol Optical Thickness
Monte Carlo simulations using Py6S
LandsatAERONET sample
Simulate with AOT

## Slide 17: Link HOT to Aerosol Optical Thickness
Calculate HOT and link with AOT

## Slide 18
Estimate PM2.5 from AOT
Use conversion factors:
From global simulations
Monthly climatology
from van Donkelaar et al. (2010)

## Slide 19
MODIS (10km)

## Slide 20
MAIAC (1km)

## Slide 21
HOTBAR (30m)

## Slide 22
PM2.5 (median error)
  HOTBAR vs ground sites 6.0μg m-3
  Ground instrument (for comparison) 2.5μg m-3
  Global 10km analysis (van Donkelaar, 2010) 6.7μg m-3
AOT Validation
Validation shows robust performance
MODIS 10km data: 60% within ± 0.13
OMI 15km data: RMSE = 0.15
Error comparable to other methods, but at 100,000 times the resolution of MODIS 10km

## Slide 25
Census output areas
to link with health data

## Slide 26
Schools
to estimate exposure around sites with vulnerable people

## Slide 27
Ongoing production of a global product, in association with
Includes extension to Landsat 8 & operationalisation
Applications
  PM2.5 mapping for exposure estimation
  Linking to health data
  Combining ground data & other satellite data to get ‘the best of all worlds’
Ongoing work

## Slide 28
Any questions?
r.t.wilson@soton.ac.uk @sciremotesense